## Slide 1
SYSTEM-DRIVEN HARDWARE DESIGN
24GHz-Radar for Movement Detection
Rakshitha Kukke Prakash 1127988
Henrique Rangan 1130830
Group C5

## Slide 2
AGENDA
03
Statemachine
02
Exercises
01
PCB Schematic
06
CFAR
05
FFT on PSoC
04
FFT on Matlab

## Slide 3
SYS-Architecture: Signal Flow Diagram to implement the objective
System function: A 24 GHz radar detects movements and signals this by turning on a red LED, as long as a movement is detected.

## Slide 4
PCB CIRCUIT
Description: PCB front side implemented in KiCAD
Description: PCB back side implemented in KiCAD

## Slide 5
PCB LAYERS
Description: PCB Back Layer for DATA
Description: PCB front Layer for DATA
Description: PCB GND Layer
Description: PCB PWR Layer

## Slide 6
PCB SCHEMATIC
Description: Circuits implemented in PCB in KiCAD

## Slide 7
AMPLIFIER CIRCUIT
1st STAGE:
Av = 100
fl = 15.392 Hz
fh = 482.287 Hz
fc = 86.15 Hz
2nd STAGE:
Av = 3
fl = 1.0261 Hz
fh = 482.287 Hz
fc = 22.245 Hz
Description: Amplifier Circuit in KiCAD

## Slide 8
Output of Stage 1:
To determine the corner frequencies of the first stage, we use the formula to calculate upper and lower cut-off frequency,
Given: Voltage Gain Av = 100
R4 = 220kOhm
=> R1 = R4/ Av
=> R1 = 2.2k Ohm
f=1/2*pi*R*C
corner frequency: fc= sqrt(fl*fh)
=> fl = 15.392 Hz
=> fh = 482.287 Hz
=> fc = 86.15 Hz

## Slide 9
Output of Stage 2:
To determine the corner frequencies of the stage 2, we use the formula f=1/2*pi*R*C and fc= sqrt(fl*fh)
Given: Voltage Gain Av = 3
R6 = 100kOhm
=> R5 = R6/ Av
=> R5 = 33.33kOhm
Note: Since 33.33k is not a standard E24 series resistor, we will be using a 33kOhm Resistor
fc= sqrt(fl*fh)
=> fl = 1.0261 Hz
=> fh = 482.287 Hz
=> fc = 22.245 Hz

## Slide 10
Measured cutoff
fc1 = 17Hz
fc2 = 362Hz

## Slide 11
VOLTAGE DIVIDER
Description: Voltage Divider implemented in PCB in KiCAD
VOLTAGE DIVIDER:
Divided by 2;
Capacitor: to stabilize the signal input and filter Noise;
Vin Test Point;
Gnd Test Point.

## Slide 12
PSoC AND RADAR INTERFACE
Description: Radar Interface implemented in PCB in KiCAD
Description: Arduino Pins implemented in PCB in KiCAD
Arduino Pins:
To connect the PCB on the PSoC;
Radar Interface:
3 Pins for Vcc, Signal input and Gnd;

## Slide 13
LEDS AND BUTTON
Description: Power Supply LED implemented in PCB in KiCAD
Description: LEDs implemented in PCB in KiCAD
Used for debugging (identifying current state of statemachine) and identify if a target is detected
Description: Push-Button implemented in PCB in KiCAD

## Slide 14: Software Development on PSoC Statemachine implementation
Objective:
To test the performance of an amplifier using the FreeSoC 2 platform and a MATLAB script for data acquisition and control.
The task is to use a DAC, which provides the test signal. Use a 16-bit SD-ADC to sample the voltage divider output and store the samples in an array. If Matlab requests by UART, send the ADC sampled data by UART to Matlab. This is repeated 10 times before the Matlab Script terminates.

## Slide 15
Automatic periodic waveform generation, here sine wave of 3V peak-peak
Input signal of the test bench
DAC updates the output value 10,000 times per second (Sample rate – 10kSPS)
Software Component
Waveform DAC

## Slide 16
It provides a low-power, low-noise front end for precision measurement applications;
In Input Range as Vssa to Vdda an external reference is not used;
Continuous Sample mode to measure a single input signal
Delta Sigma Analog to Digital Converter

## Slide 17
ADC is inherently differential
Single-ended mode is implemented by internally connecting the negative input to ground.
Delta Sigma Analog to Digital Converter

## Slide 18
The UART provides asynchronous communications commonly referred to as RS232 or RS485;
The UART Component can be configured for Full Duplex, Half Duplex, RX only, or TX only versions;
The main reason for this to be used was to transmit the adc data to MATLAB and receive ‘s’ character.
Universal Asynchronous Receiver Transmitter (UART)

## Slide 19
PINS CONFIGURATIONS AND SETUP

## Slide 20: Statemachine – implemented using switch case

## Slide 21: Software Development on PSoC
An array for storing ADC data is declared and initialized to 0.
SAMPLES is a macro defined to be the size of the data i.e 1024
An initialize function is called before starting the statemachine, which initializes all the software components used, for example, the UART, DAC, ADC, ISRs
2 ISRs are used: An interrupt is generated at the falling edge of the button press and another when the UART receives any data.

## Slide 22
Statemachine header
An enum for the different states of the statemachine is defined.
3 states idle, sampling and UART_transfer are used in the switch-case statemachine implementation
The function definitions are also defined in the header:
Init_func() as mentioned in previous slide initializes all the software components
The statemachine function takes a pointer to the array that stores ADC samples as a parameter
An ISR function prototype is used to declare the ISR. An interrupt is raised when the character ‚s‘ is received by the UART.
Interrupt function CY_ISR_PROTO sets a buttonPressed variable to 1 if the PushButton is pressed.

## Slide 23
ISR
Isr_UART is an ISR function that sets a variable to 1 if a character ‚s‘ is received from the MATLAB script by the UART.
Isr_pushButton is an ISR function that sets the varibale ButtonPressed to 1 when the push button is pressed. At the falling edge of the push button, an isr is generated.

## Slide 24
Statemachine code
The LEDs are used to indicate the current state of the system.
Idle state
  The Red LED is used to indicate that the system is in the idle state.
  a counter is initialized to 0
  If a button is pressed, a state transition is initiated.
  The state is modified to SAMPLING and the buttonPressed variable is set back to 0.
Sampling state
  The Orange LED is used to indicate that the system is in the SAMPLING state
  The ADC_DelSig_IsEndConversion function checks the status that the most recently started conversion has completed
  ADC_DelSig_WAIT_FOR_RESULT - Does not return until ADC conversion is complete.
  ADC_DelSig_GetResult32 returns the result of the last ADC conversion, which is stored in an array
  If a character ‘s’ is received, a state transition is initiated

## Slide 25
Statemachine code
UART_TRANSFER state
  The Green LED is used to indicate that the system is in the UART_TRANSFER state
  The system sends ADC samples over UART.
  It iterates over the ‘adcArray’ containing 1024 samples.
  For each sample, it sends the lower and upper 8 bits over UART using the UART_PutChar function.
  The ‚count‘ variable is incremented to keep track of the number of data transfers.
  The system waits for the reception of the 'o' character through UART.
  The ‘do-while’ loop is used to continuously call ‘UART_GetChar’ until the 'o' character is received.
  If the count is less than 10, a state transition is initiated.
  The state is modified to SAMPLING.
  If the count equals 10, a state transition is initiated.
Default state
  The system defaults to the IDLE state if an undefined state value is encountered.

## Slide 26
FFT
1.Transform to Frequency Domain:
The FFT converts a signal from its original time domain into the frequency domain. This process decomposes the signal into its constituent frequencies.
2. Identify Noise Components:
In the frequency domain, noise and the desired signal components can often be distinguished. Noise is usually spread across a wide range of frequencies, while the desired signal might occupy a specific frequency range.
3. Apply a Filter:
Once the noise frequencies are identified, a filter can be applied to remove or reduce these unwanted components. Common filters used in this context include low-pass, high-pass, band-pass, and band-stop filters.
4. Inverse FFT:
After filtering the unwanted frequencies, the inverse FFT (IFFT) is applied to convert the signal back to the time domain. The result is a signal with reduced noise.

## Slide 27
MATLAB script for receiving ADC data from PSoC and plotting it on a graph

## Slide 28
OUTPUT of FFT on MATLAB

## Slide 29
The code for the IDLE and SAMPLING states remain the same
UART_TRANSFER state
  The Green LED is used to indicate that the system is in the UART_TRANSFER state.
  The Fast Fourier Transform is performed on the ADC samples that are present in the ‘adcArray’
  It processes the adcArray which contains 1024 samples.
  The FFT results are sent over UART. For each element in fftArray:
  UART_PutChar(fftArray[i]) sends the least significant byte.
  UART_PutChar(fftArray[i] >> 8) sends the second byte.
  UART_PutChar(fftArray[i] >> 16) sends the third byte.
  UART_PutChar(fftArray[i] >> 24) sends the most significant byte. This sends a total of 2048 bytes (4 bytes per element in fftArray)
  The ‘do-while’ loop is used to continuously call ‘UART_GetChar’ until the 'o' character is received.
  If the count is less than 10, a state transition is initiated to SAMPLING state.
  If the count equals 10, a state transition is initiated.
Statemachine code for FFT implementation on PSoC

## Slide 30
MATLAB script for receiving ADC and FFT data from PSoC and plotting it on a graph

## Slide 31
OUTPUT of FFT from PSoC

## Slide 32
IPM 165 - 24 GHz CW Radar
The IPM-165 is a 24GHz Doppler module with an asymmetrical wide beam for detection of moving objects
CFAR (Constant False Alarm Rate) is a signal processing technique commonly used in radar systems and other detection systems to automatically adjust the detection threshold, ensuring a consistent rate of false alarms despite varying levels of background noise or clutter. The main goal of CFAR is to maintain a constant probability of false alarms, which is crucial for reliable detection of targets.
CFAR

## Slide 33
CA-CFAR
Adaptive Threshold Setting:
The detection threshold is adaptively set as a function of the estimated noise level. For instance, in CA-CFAR, the threshold TTT is typically set as:
T=α⋅Noise Estimate
Where α is a scaling factor determined by the desired false alarm rate.
Cell under test (CUT) is xi • Noise in the CUT determines the threshold • The noise parameters in the CUT has to be estimated (here: σw^2)

## Slide 34
CA-CFAR
With:
N : number of averaged cells
PFA : target false alarm probability
The video shows the output of the 2nd stage
of the amplifier, with the radar module
connected.

## Slide 35
Spectral Representation of a Test signal generated in MATLAB
The Green dots on the spectrum indicates the detected targets

## Slide 36
Matlab code for pre-recorded RADAR data

## Slide 37
Sample set 1
Sample set 2

## Slide 38
MATLAB CA-CFAR implementation

## Slide 39
CA-CFAR included in the statemachine
LED red glows when target is detected

## Slide 40
THANK YOU

## Slide 41: Software Development on PSoC
Exercise 1: UART Talkback
  Develop a software on the PSoC, which receives the data from a terminal program on the windows and writes it back to the terminal in capital letters.
  Step1: Write Back the text
  Step2: Capitalize it

## Slide 42: Software Development on PSoC
The UART receives characters from the terminal and transfers the character back to the terminal

## Slide 43: Software Development on PSoC
Method 1 and 2 mentioned above produce the same result of capitalizing the text and writing back onto the terminal.
Method 1 checks if every character that is received through the UART is a lowercase aphabet and it subtracts 32 from the character to generates its corresponding Upper case in ascii
Method 2 checks if the received character is not null and uses “toupper” function which converts the lowercase alphabet to upper case and displays on the terminal

## Slide 44
Expected Behaviour:
1. sends 's' over the serial Port
2. Waits until there are 256 bytes in the buffer
3. If there 256 bytes in the buffer, it take them, calculates the fft out of it and displays the received data and the absolute of the fft.
Wave Generation in PSoC

## Slide 45: Wave Generation in PSoC
TRIANGLE WAVE GENERATION
SQUARE WAVE GENERATION

## Slide 46: Wave Generation in PSoC
SAWTOOTH WAVE GENERATION
STEP WAVE GENERATION